## Pin

| Pin | Function | ESP-8266 Pin |
| --- | --- | --- |
| TX | TXD | TXD |
| RX | RXD | RXD |
| A0 | Analog input, max 3.3V input | A0 |
| D0 | IO | GPIO16 |
| D1 | IO, SCL | GPIO5 |
| D2 | IO, SDA | GPIO4 |
| D3 | IO, 10k Pull-up | GPIO0 |
| D4 | IO, 10k Pull-up, BUILTIN_LED | GPIO2 |
| D5 | IO, SCK | GPIO14 |
| D6 | IO, MISO | GPIO12 |
| D7 | IO, MOSI | GPIO13 |
| D8 | IO, 10k Pull-down, SS | GPIO15 |
| G | Ground | GND |
| 5V | 5V | - |
| 3V3 | 3.3V | 3.3V |
| RST | Reset | RST |

All IO have interrupt/pwm/I2C/one-wire supported(except D0)

## Programming

The D1 mini has a micro USB for auto programming.
Also you can programming it using OTA.

## Warnings

All IO is work at 3.3V.

### Installing Hardware package

There is two ways to install hardware package, Boards Manager and git.

#### Installing with Boards Manager

Starting with 1.6.4, Arduino allows installation of third-party platform packages using Boards Manager. We have packages available for Windows, Mac OS, and Linux (32 and 64 bit).

1. Install Arduino 1.6.7 from the Arduino website.

2. Start Arduino and open Preferences window.

3. Enter

http://arduino.esp8266.com/stable/package_esp8266com_index.json

into Additional Boards Manager URLs field.

You can add multiple URLs, separating them with commas.

4. Open Tools→Board:xxx→Boards Manager and install esp8266 by ESP8266 Community

(and don't forget to select your ESP8266 board from Tools > Board menu after installation).

#### Installing use git (Recommend)

We recommend using git to install Hardware package, you can always get the latest version of it.

##### Install Arduino

Install Arduino 1.6.7 from the Arduino website.

##### Clone repository

Clone repository into Sketchbook_directory/hardware/esp8266com/esp8266 directory (or clone it elsewhere and create a symlink), you may need to create the hardware directory if it does not exist.

cd hardware

mkdir esp8266com

cd esp8266com

git clone https://github.com/esp8266/Arduino.git esp8266

You should end up with the following directory structure:

─┬ Arduino

└─┬ hardware

└─┬ esp8266com

└─┬ esp8266

├── bootloaders

├── cores

├── doc

├── libraries

├── package

├── tests

├── tools

├── variants

├── platform.txt

├── programmers.txt

├── README.md

├── boards.txt

├── LICENSE

##### Download binary tools

cd esp8266/tools

python get.py

##### Restart the Arduino IDE

To get the latest version anytime, in Sketchbook_directory/hardware/esp8266com/esp8266 simply run

git pull

##### Restart the Arduino IDE

To get the latest version anytime, in Sketchbook_directory/hardware/esp8266com/esp8266 simply run

git pull

##### Configure Board

After install hardware package, you will see WeMos boards in the Tools→Board:xxx

Choose your own board.

Upload Using:

Serial – Use USB port on board to upload flash

OTA – Use OTA to upload flash

CPU Frequency:

80MHz

160MHz

Flash Size:

4M (3M SPIFFS) – 3M File system size

4M (1M SPIFFS) – 1M File system size

Upload Speed:

921600 bps – recommend

### Installing Examples

#### Simple Way

- Download Examples files form here.

- Rename the uncompressed directory to D1_mini_Examples

- Move directory to Sketchbook_directory

- The path will look like Sketchbook_directory/D1_mini_Examples

- Restart the Arduino IDE

- All examples are under File→Sketchbook→D1_mini_Examples

#### Git Way (Recommend)

We recommend using git to install Examples, you can always get the latest version of it.

- Clone repository into Sketchbook_directory directory (or clone it elsewhere and create a symlink).

cd Sketchbook_directory

git clone https://github.com/wemos/D1_mini_Examples.git